## Slide 1
Edge Detection – Canny Algorithm

## Slide 2
What is an Edge?
Discontinuity in intensity
Significant change of intensity in an image
Original Image
Original Image
Edge Image
Edge Image

## Slide 3
Types of Edges
Step Edge Intensity abruptly changes
Ramp Edge Intensity change is not instantaneous, occurs over a finite distance

## Slide 4
Types of Edges – Contd.
Ridge Edge Intensity abruptly changes, but returns back to original value
Roof Edge Intensity change is not instantaneous, occurs over a finite distance

## Slide 5
Edge Detection
Edge detection is an image processing technique for finding the boundaries of objects within images
Original Image
Edge Image

## Slide 6
Use of Edge Detection
Extract important features
Divide image into areas corresponding to different objects
Extracted features used by higher level computer vision algorithms

## Slide 7
Goal of Edge Detection
Low error rate
  Accurately detect as many edge as possible
  Probability of detecting real edge points should me maximized
Well localization of detected edge points
  Operator should accurately localize on the center of the edge
Single edge point response
  One real edge should not result in more than one detected edge
  Image noise should not create false edges

## Slide 8
Edge Detectors
Robert’s Cross Operator
Sobel Operator
Prewitt Operator
Canny Edge Operator

## Slide 9
Overview – Canny Edge Detector
Developed by John F. Canny in 1986
Less Sensitive to noise
Offers good localization of edges
Utilizes gradient of the edge to generate thin, one-pixel wide edges
Also know as optimal detector

## Slide 10
Steps - Canny Edge Detector
Smoothing
    Process of removing noise
    To prevent false edge detection necessary to filter not noise
    Gaussian filter applied to convolve with the image

## Slide 11
Steps - Canny Edge Detector
Find intensity gradients
    Process of finding intensity gradient of the image
    Edge detector operator is used which returns a value for the first derivative in the horizontal direction (Gx) and the vertical direction (Gy)

## Slide 12
What Next?

## Slide 13
Steps - Canny Edge Detector
Non Maxima Suppression
    Process of edge thinning

## Slide 14
What Next?

## Slide 15
Steps - Canny Edge Detector
Hysteresis Thresholding
    Process of determining potential edges
    Set low and high threshold values

## Slide 16
Implementation

## Slide 17
Implementation

## Slide 18
Implementation

## Slide 19
Thank You